## During Class Notes

Pipelining
-

Logical core – a kind of virtual core; allows more multithreading on a single core, the example given is 2 logical cores run on a single core
- as far as the computer is aware, there are 2 cores, but physically there is only one

Flynn’s Taxonomy
- SiSD – single instruction, multiple data
- parallelism achieved by dividing data among processors.
- This is what data parallelism is.
- SIMD

Interconnect – is in charge of the routing of data

Shared memory interconnects
- Bus interconnect
- - a collection of parallel communication wires together with some hardware that controls access to the bus.
- Communication wires are shared by the devices that are connected to it
- As the number of devices connected to the bus increases, contention for use of the bus increases, and performance decreases.
- Switched interconnect
Uses switches to control the routing of data among the connected devices.
Crossbar
- Allows simultaneous connection among different devices
- Faster than buses
- But the cost of switches and links is relatively high
  - he means this in the financial sense; switches and links are financially expensive

Memory wall problem – huge delay to get data from the main memory to the CPU
- solution, get small memory near the CPU called a cache

Distributed memory interconnects
- Two groups
- direct interconnect
  - Each switch is directly connected to a processor-memory pair, and the switches are connected to each other.
- indirect interconnect
  - Switches may not be directly connected to a processor.

Bisection width
- A measure of “number of simultaneous communications” or “connectivity”.
- How many simultaneous communications can take place “across the divide” between the halves?

Latency – the time that elapses between the source’s beginning to transmit the data and the destination’s starting to receive the first byte

Bandwidth – the rate at which we are sending the data

Message transmission time = L + n/ b

L = Latency (seconds)

n = length of message (bytes)

b = bandwidth (bytes/second)

Cache coherence
- Programmers have no control over caches and when they get updated
- Each core has its own cache; so even shared variables may not always appear to be shared in practice. See the cache coherence example, explain why z1 may not be 28 and may be 8.
## After Class Notes
Lecture slides: 02.pdf, 03.pdf
#### Terms
Register – on-board storage on the CPU, very fast because it’s on the CPU
Program Counter – stores address (in Program Memory) of the next instruction to be executed
Bus – wires and hardware that connects the CPU and memory
Process – An instance of a program being executed
- Memory
  - Program – the actual program loaded into memory
  - Data – the data that the program uses
- Security
- State
  - Register values – the values in the registers
  - Program counters – the address of the next instruction
  - Resources (file handlers, sockets)